## Slide 1: Raster Analysis—Part 2
<number>
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 2: Desired Learning Objectives
<number>
Describe application of the following raster functions:
  Reclassification
  Surface functions
  Distance functions
  Density functions
  Interpolation
  Neighborhood functions
  Zonal functions
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 3: Other raster analysis techniques
<number>
Reclassification
Surface functions
Distance functions
Density functions
Interpolation
Neighborhood functions
Zonal functions
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 4: Reclassify
<number>
Convert one set of grid values to another
Manual or classify
Slope
Hi slope/lo slope
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 5: Surface analysis
<number>
DEM
Slope
Aspect
Hillshade
Contouring
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 6: Slope function
<number>
Calculates slope of the surface based on surrounding cells
Can be expressed in degrees or percent
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 7: Aspect function
<number>
Calculates direction of steepest slope, e.g. which way the slope “faces”
Value represents direction from 0 degrees to 360 degrees, where 0/360 is North
Flat areas are assigned a -1 value
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 8: Hillshade
<number>
Calculates the brightness or illumination of a surface from a specified light source
Applications include terrain display and modeling satellite reflectance
Azimuth is direction of illumination source (315 by default)
Altitude is the angle of the source above the horizon (45 deg)
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 9: Viewshed analysis
<number>
Calculate areas visible from a set of observation points
Additional parameters are available for the tool version, such as the horizontal angle included
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 10: Cut and fill on a site
<number>
[Initial surface] – [final surface]
Cut
Fill
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 11: Hydrologic functions
<number>
Derive streams, watersheds, and other hydrologic features based on analysis of a DEM.
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 12: Distance functions
<number>
Straight line distance
Cost path distance
Buffers
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 13: Straight line distance
<number>
Starts from a set of features (points, lines, polygons)
Creates a grid where each cell represents distance to the closest of the features
Distance units are given in coordinate system map units
Distance to roads (meters)
The distance function is the first step in in creating raster buffers.
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 14: Lowest cost path
<number>
1. Create start/stop shapefiles
Create cost grid
Calculate cost distance grid and cost direction grid
Find lowest cost path
Elevation
Slope
Cost distance
Cost direction
Notes: Mastering ArcGIS
Chapter 15
<number>

## Slide 15: Raster Analysis— End of Part 2
<number>
Notes: Mastering ArcGIS
Chapter 15
<number>