## Slide 1: Why do we need to test the water quality? what are we looking for? Which parameters?
By: Prof. Eqrar
Training course of Field Kit Testing |  | 

## Slide 2: Why study water quality
Groundwater quality for use – public health, Irrigation, ecotoxicology, suitability for industrial processes etc..
Groundwater as an environmental agent – discharge of contaminants to sensitive environments..
Tool for understanding groundwater flow processes, interaction with the environment..

## Slide 3: Water sampling plan around the following questions .
Why are you field sampling?
Who will use your data?
How will the data be used?
What data quality do you require?
What methods will you use?
How will the sample be preserved?
Who will be involved and how?
How will the data be managed and reported?
How will you ensure your data are credible?
Do NOT go to the field without a plan!

## Slide 4: Why water sampling
Identification of the aquifers intercepted by water bores
Assessment of groundwater movement and flow patterns
Understanding of recharge-discharge mechanisms
Determination of the nature of surface water and groundwater interconnectivity
Identification of the magnitude, sources and transport of salt, nutrients, pesticides and other contaminants
Understanding of the evolution of the groundwater chemistry and flow patterns, and possible causes for groundwater quality changes
Assessment of the impact of land use changes, irrigation and groundwater extraction on the regional groundwater quantity and quality
Developing groundwater as an effective sampling medium for mineral exploration

## Slide 5: Water Use
Use | Typical quality parameters
Public Water Supply | Turbidity, TDS, inorganic and organic compounds, microbes
Water contact recreation | Turbidity, bacteria, toxic compounds
Fish propagation and wildlife | DO, chlorinated organic compounds
Industrial water supply Power generation: Sewage water | Suspended and dissolved constituents Turbidity NO3,PO4,BO2….
Agricultural water supply | Sodium, TDS
Shellfish harvesting | DO, bacteria

## Slide 6: Categories of Contaminants
Chemicals
Organic
Inorganic
Microbiological
  Bacteria
  Virus
  Protozoa
  Helminths
Physical
Turbidity
Colour
Odor
Taste

## Slide 7: Global Water Use Growth
“In 2007 we (Americans) spent $16 billion on bottled water. That’s more than we spent on iPods or movie tickets”

## Slide 8: Size Comparison
Virus (0.02 to 0.2 micron)
Helminth
40 to 100 microns
Pore size in a sand filter (1 micron)
Smallest
Largest
Virus
Bacteria
Protozoa
Helminth
Bacteria (0.2 to 5 microns)
Protozoa
4 to 20 microns
Notes: Representation of the relative sizes of different pathogens, and the pore size in a sand filter.
Pathogen size is very relevant to understanding filter technology.

## Slide 9: Physico-chemical Parameters
  Field Measured Parameters
pH
Specific conductance (EC)
Salinity
    Alkalinity
Total dissolved solids (TDS)
Turbidity
Dissolved oxygen (DO)
Temperature

## Slide 10
Turbidity meter
pH / °C / mV Meter
Conductivity / TDS / °C Hand Held Meter
Portable photometer
Colour Comparator Kit
Syringe devices
Plopper/sampler and tape measure
Water level meter
Digital titrator for measuring alkalinity

## Slide 11: Water chemical constituents
Minor Constituents (0.01-10mg/l)
  B
  K
  F
  Sr
  Fe
  CO32- - carbonate
  NO3- - nitrate
Major Constituents (> 5 mg/L)
  Ca
  Mg
  Na
  Cl
  Si
  SO42- - sulfate
  H2CO3 - carbonic acid
  HCO3- - bicarbonate
Trace Constituents (< 0.1 mg/l)
  Al
  As
  Ba
  Br
  Cd
  Co
  Cu
  Pb
  Mn
  Ni
  Se
  Ag
  Zn
  others
Water chemical parameters for:
-Hydrogeologist(drinking water standard)
-Water engineers
- Irrigation Engineers(irrigation water standard)
Environmental Engineer
Waste water expert
Mechanical Engineer(industrial)
(industrial water standard)

## Slide 14: Non suitablaty of water quality