## Slide 1: Adding the third dimension
In high relief areas variables such as altitude, aspect and slope strongly influence both human and physical environments
  a 3D data model is therefore essential
  use a Digital Terrain Model (DTM)
  derive information on:
    height (altitude), aspect and slope (gradient)
    watersheds (catchments)
    solar radiation and hill shading
    cut and fill calculations
    etc.

## Slide 2: DEMs and DTMs
Some definitions…
  DEM (Digital Elevation Model)
    set of regularly or irregularly spaced height values
    no other information
  DTM (Digital Terrain Model)
    set of regularly or irregularly spaced height values
    but, with other information about terrain surface
    ridge lines, spot heights, troughs, coast/shore lines, drainage lines, faults, peaks, pits, passes, etc.

## Slide 3: UK DEM data sources
Ordnance Survey:
  Landform Panorama
    source scale: 1:50,000
    resolution: 50m
    vertical accuracy: ±3m
  Landform Profile
    source scale: 1:10,000
    resolution: 10m
    vertical accuracy: ±0.3m

## Slide 4: Comparison
Landform Panorama
Landform Profile

## Slide 5: LIDAR data (LIght Detection And Ranging)
Horizontal resolution: 2m
Vertical accuracy: ± 2cm

## Slide 6: Modelling building and topological structures
Two main approaches:
  Digital Elevation Models (DEMs) based on data sampled on a regular grid (lattice)
  Triangular Irregular Networks (TINs) based on irregular sampled data and Delaunay triangulation

## Slide 7: DEMs and TINs
DEM with sample points
TIN based on same sample points

## Slide 8: Advantages/disadvantages

## Slide 9: Derived variables
Primary use of DTMs is calculation of three main terrain variables:
  height
    altitude above datum
  aspect
    direction area of terrain is facing
  slope
    gradient or angle of terrain

## Slide 10: Calculating slope
Inclination of the land surface measured in degrees or percent
  3 x 3 cell filter
  find best fit tilted plane that minimises squared difference in height for each cell
  determine slope of centre (target) cell
  Slope = b2 + c2
10
8
9
8
8
7
7
6
5
z = a + bx + cy

## Slide 11: Calculating aspect
Direction the land surface is facing measured in degrees or nominal classes (N, S, E, W, NE, SE, NW, SW, etc.)
  use 3 x 3 filter and best fit tilted plane
  determine aspect for target cell
Aspect = tan-1 c / b
10
8
9
8
8
7
7
6
5

## Slide 12: Other derived variables
Many other variables describing terrain features/characteristics
  hillshading
  profile and plan curvature
  feature extraction
  etc.

## Slide 13: Examples
height
slope
aspect
hillshading
plan curvature
Feature extraction

## Slide 14: Terrain visualisation
Analytical hillshading
Orthographic views
  any azimuth, altitude, view distance/point
  surface drapes (point, line and area data)
Animated ‘fly-through’
What if? modelling
  photorealism
  photomontage
  CAD

## Slide 15: Examples of hillshading and orthographic projection
Hillshading
DEM
Orthographic projection

## Slide 16: Example surface drape
DEM
Rainfall
Draped image