## Slide 1: NORPLAN GIS Development (Faryab Province)
By: M Shuaib Zarinkhail
GIS-MIS Advisor
NORPLAN, RuWatSIP, MRRD

## Slide 2: Work focus is Faryab Province

## Slide 3: Faryab Districts

## Slide 4: Project Geographical Information System (GIS)
The project focuses on Faryab province in north
  This work will further be used as an example for other places and provinces
Data types required for NORPLAN
  Groundwater points data including
    Different types of wells (dug well, bore well, …)
  Springs feeding pipe networks
  Karezes
  Geological and hydrogeological base-maps
  Some additional hydrological data (river flows, rainfall)
  Groundwater quality data (measurements, tests, …)

## Slide 5: Groundwater Points Data
Groundwater points data for the whole country do exist
  This data is combined by WASH cluster and submitted to the RuWatSIP in MRRD
Different organizations are working in this area from more than 20 years
Some of these organizations work in Faryab province
  i.e. DACAAR, INTERSOS, NCA, NSP, SCA, RuWatSIP (MRRD)
Extracted data from old Soviet maps

## Slide 6: Groundwater Points Data (# of records)
The following figures show number of records for groundwater points up to date
  Total groundwater points in the country ~ 135,000
  Groundwater points in Faryab ~ 3,300
This existing data is in different formats
  Only limited details, shown below, can be found in all
    Organization, Water Point Type, Construction Year, GPS Coordinates, Depth, Pump Type (if have hand pumps)

## Slide 7: Groundwater Points Data (GPS data)
One of the important part in such data is the GPS (Global Positioning System) coordinates
  With the GPS coordinates, data can be shown on geographical maps
GPS data is not recorded for all the groundwater points
  Out of above, about 42,000 groundwater points have GPS coordinates
  About 2,800 of groundwater points in Faryab province have GPS coordinates and can be shown on GIS maps

## Slide 8: Faryab Well Depths Map

## Slide 9: Gurziwan District, Faryab - Well Depths

## Slide 10: Groundwater Points Data (group data)
Another issue in this data is that some groundwater points are reported as groups
  Those of grouped groundwater points that have GPS coordinates, they have only one point with (x,y) coordinates
  Such data can only be shown under one symbol (point) on a map layer which is still fine for some activities

## Slide 11: Gurziwan District, Faryab - Grouped Wells

## Slide 12: Groundwater Points Data (raw data)
We can call this existing data the raw data
  The raw data need further clearance and check for accuracy
During the planning phase of the NORPLAN project, our international colleagues had worked on Faryab raw data
Some records are clarified and ready to use in project database
  About 1,200 records are ready for entry to project database

## Slide 13: Groundwater Quality Data
Water quality data is another aspect
NORPLAN needs to record the following to represent groundwater quality data on GIS maps
  Measurement record
  Water test record
    Different kinds of tests can be implemented and recorded
  Maintenance record
  Monitoring record

## Slide 14: Groundwater Points Data (database)
A geodatabase needs to develop and store the clarified data for Faryab
Attributes for such data are:
  Groundwater Points, Electrical Conductivity, Construction Details, Static Water Level, Yield – Drawdown Relation, Flow Rate, etc
Further analysis will be done based on this data and using these formats as a template

## Slide 15: UNICEF Plans and Expectations
Explanations by WASH Specialist from UNICEF, Mr Adane Bekele

## Slide 16: The Way Forward
One of the goals of NORPLAN is to develop a hydrogeological map atlas and disseminate hydrogeological information in this atlas
For this, close coordination with the RuWatSIP as well as other organizations that involve in similar activities is required
Data stream and deliver trainings in such activities can help the NORPLAN to achieve this target

## Slide 17: The Way Forward (Future Plan)
In our plan, we have the following 3 main activities
  Develop geodatabase (s) to record and represent project data on GIS (2013)
  Combine geological and hydrogeological map atlases for Faryab in PDF and make them available online (2013)
  Develop an ad-hoc online system to represent a web atlas for Faryab province (2014)

## Slide 18: The Way Forward (Future Plan)
Project databases will be based on technical data formats clarified by technical sources of the project
Technical maps for Faryab province in general and for Faryab districts individually will be prepared
  Such sets of maps will be combined in portable files and shared with stakeholders via project web site http://www.norplan.af

## Slide 19: The Way Forward (Future Plan)
The final work of NORPLAN in this regard will be disseminating information via an online system
  The system will have an interface with a bunch of options to select different arguments on map
The following slides show screen shots of a similar system

## Slide 20: Sample System

## Slide 21: Sample System (Map Layers Menu)

## Slide 22: Sample System (ad-hoc information)

## Slide 23: Sample System (measurment)

## Slide 24: Thank you for attention! Next is group discussion:
Organization of data capture at both local and provincial levels?
Who, where to collect, check and enter data?
What format and information would be desired by users of GIS?
How should the information be presented to be most useful?
improvements on proposed approach?